## Slide 1
Lecture: Metrics, Benchmarks, Performance
Topics: benchmark suites, summarizing performance,
performance equations
HW1 due Wednesday 1:25pm (+ 1.5 day auto extension)

## Slide 2
Measuring Performance
Two primary metrics: wall clock time (response time for a
program) and throughput (jobs performed in unit time)
To optimize throughput, must ensure that there is minimal
waste of resources

## Slide 3
Benchmark Suites
Performance is measured with benchmark suites: a
collection of programs that are likely relevant to the user
  SPEC CPU 2017: cpu-oriented programs (for desktops)
  SPECweb, TPC: throughput-oriented (for servers)
  EEMBC: for embedded processors/workloads

## Slide 4
Summarizing Performance
Consider 25 programs from a benchmark set – how do
we capture the behavior of all 25 programs with a
single number?
P1 P2 P3
Sys-A 10 8 25
Sys-B 12 9 20
Sys-C 8 8 30
  Sum of execution times (AM)
  Sum of weighted execution times (AM)
  Geometric mean of execution times (GM)

## Slide 5
Sum of Weighted Exec Times – Example
We fixed a reference machine X and ran 4 programs
A, B, C, D on it such that each program ran for 1 second
The exact same workload (the four programs execute
the same number of instructions that they did on
machine X) is run on a new machine Y and the
execution times for each program are 0.8, 1.1, 0.5, 2
With AM of normalized execution times, we can conclude
that Y is 1.1 times slower than X – perhaps, not for all
workloads, but definitely for one specific workload (where
all programs run on the ref-machine for an equal #cycles)

## Slide 6
GM Example
Computer-A Computer-B Computer-C
P1 1 sec 10 secs 20 secs
P2 1000 secs 100 secs 20 secs
Conclusion with GMs: (i) A=B
(ii) C is ~1.6 times faster
For (i) to be true, P1 must occur 100 times for every
occurrence of P2
With the above assumption, (ii) is no longer true
Hence, GM can lead to inconsistencies

## Slide 7
Problem 4
Consider 3 programs from a benchmark set. Assume that
system-A is the reference machine. How does the
performance of system-B compare against that of
system-C (for all 3 metrics)?
P1 P2 P3
Sys-A 5 10 20
Sys-B 6 8 18
Sys-C 7 9 14
  Sum of execution times (AM)
  Sum of weighted execution times (AM)
  Geometric mean of execution times (GM)

## Slide 8
Problem 4
Consider 3 programs from a benchmark set. Assume that
system-A is the reference machine. How does the
performance of system-B compare against that of
system-C (for all 3 metrics)?
P1 P2 P3 S.E.T S.W.E.T GM
Sys-A 5 10 20 35 3 10
Sys-B 6 8 18 32 2.9 9.5
Sys-C 7 9 14 30 3 9.6
  Relative to C, B provides a speedup of 1.03 (S.W.E.T)
  or 1.01 (GM) or 0.94 (S.E.T)
  Relative to C, B reduces execution time by
  3.3% (S.W.E.T) or 1% (GM) or -6.7% (S.E.T)

## Slide 9
Summarizing Performance
GM: does not require a reference machine, but does
not predict performance very well
  So we multiplied execution times and determined
  that sys-A is 1.2x faster…but on what workload?
AM: does predict performance for a specific workload,
but that workload was determined by executing
programs on a reference machine
  Every year or so, the reference machine will have
  to be updated

## Slide 10
Speedup Vs. Percentage
“Speedup” is a ratio = old exec time / new exec time
“Improvement”, “Increase”, “Decrease” usually refer to
percentage relative to the baseline
= (new perf – old perf) / old perf
Note that performance is proportional to 1 / exectime
A program ran in 100 seconds on my old laptop and in 70
seconds on my new laptop
  What is the speedup? (1/70) / (1/100) = 1.42
  What is the percentage increase in performance?
  ( 1/70 – 1/100 ) / (1/100) = 42%
  What is the reduction in execution time? 30%

## Slide 11
CPU Performance Equation
Clock cycle time = 1 / clock speed
CPU time = clock cycle time x cycles per instruction x
number of instructions
Influencing factors for each:
  clock cycle time: technology and pipeline
  CPI: architecture and instruction set design
  instruction count: instruction set design and compiler

## Slide 12
Problem 5
My new laptop has an IPC that is 20% worse than my old
laptop. It has a clock speed that is 30% higher than the old
laptop. I’m running the same binaries on both machines.
What speedup is my new laptop providing?

## Slide 13
Problem 5
My new laptop has an IPC that is 20% worse than my old
laptop. It has a clock speed that is 30% higher than the old
laptop. I’m running the same binaries on both machines.
What speedup is my new laptop providing?
Exec time = cycle time * CPI * instrs
Perf = clock speed * IPC / instrs
Speedup = new perf / old perf
= new clock speed * new IPC / old clock speed * old IPC
= 1.3 * 0.8 = 1.04

## Slide 14
An Alternative Perspective - I
Each program is assumed to run for an equal number
of cycles, so we’re fair to each program
The number of instructions executed per cycle is a
measure of how well a program is doing on a system
The appropriate summary measure is sum of IPCs or
AM of IPCs = 1.2 instr + 1.8 instr + 0.5 instr
cyc cyc cyc
This measure implicitly assumes that 1 instr in prog-A
has the same importance as 1 instr in prog-B

## Slide 15
An Alternative Perspective - II
Each program is assumed to run for an equal number
of instructions, so we’re fair to each program
The number of cycles required per instruction is a
measure of how well a program is doing on a system
The appropriate summary measure is sum of CPIs or
AM of CPIs = 0.8 cyc + 0.6 cyc + 2.0 cyc
instr instr instr
This measure implicitly assumes that 1 instr in prog-A
has the same importance as 1 instr in prog-B

## Slide 16
AM and HM
Note that AM of IPCs = 1 / HM of CPIs and
AM of CPIs = 1 / HM of IPCs
So if the programs in a benchmark suite are weighted
such that each runs for an equal number of cycles, then
AM of IPCs or HM of CPIs are both appropriate measures
If the programs in a benchmark suite are weighted such
that each runs for an equal number of instructions, then
AM of CPIs or HM of IPCs are both appropriate measures

## Slide 17
AM vs. GM
GM of IPCs = 1 / GM of CPIs
AM of IPCs represents thruput for a workload where each
program runs sequentially for 1 cycle each; but high-IPC
programs contribute more to the AM
GM of IPCs does not represent run-time for any real
workload (what does it mean to multiply instructions?); but
every program’s IPC contributes equally to the final measure

## Slide 18
Problem 6
My new laptop has a clock speed that is 30% higher than
the old laptop. I’m running the same binaries on both
machines. Their IPCs are listed below. I run the binaries
such that each binary gets an equal share of CPU time.
What speedup is my new laptop providing?
P1 P2 P3
Old-IPC 1.2 1.6 2.0
New-IPC 1.6 1.6 1.6

## Slide 19
Problem 6
My new laptop has a clock speed that is 30% higher than
the old laptop. I’m running the same binaries on both
machines. Their IPCs are listed below. I run the binaries
such that each binary gets an equal share of CPU time.
What speedup is my new laptop providing?
P1 P2 P3 AM GM
Old-IPC 1.2 1.6 2.0 1.6 1.57
New-IPC 1.6 1.6 1.6 1.6 1.6
AM of IPCs is the right measure.
Speedup with AM would be 1.3.

## Slide 20
Performance Metrics Summary
Performance summaries: AM of weighted exec times, GM
AM of IPCs, HM of IPCs (AM of CPIs), GM of IPCs
Speedup (ratio), performance improvement (ratio – 1)
CPU time = cycle time x CPI x #instructions