## Slide 1
Lecture: Synchronization, Consistency Models
Topics: synchronization wrap-up,
need for sequential consistency, fences

## Slide 2
Test-and-Test-and-Set
lock: test register, location
bnz register, lock
t&s register, location
bnz register, lock
CS
st location, #0

## Slide 3
Load-Linked and Store Conditional
LL-SC is an implementation of atomic read-modify-write
with very high flexibility
LL: read a value and update a table indicating you have
read this address, then perform any amount of computation
SC: attempt to store a result into the same memory location,
the store will succeed only if the table indicates that no
other process attempted a store since the local LL (success
only if the operation was “effectively” atomic)
SC implementations do not generate bus traffic if the
SC fails – hence, more efficient than test&test&set

## Slide 4
Spin Lock with Low Coherence Traffic
lockit: LL R2, 0(R1) ; load linked, generates no coherence traffic
BNEZ R2, lockit ; not available, keep spinning
DADDUI R2, R0, #1 ; put value 1 in R2
SC R2, 0(R1) ; store-conditional succeeds if no one
; updated the lock since the last LL
BEQZ R2, lockit ; confirm that SC succeeded, else keep trying
If there are i processes waiting for the lock, how many
bus transactions happen?

## Slide 5
Spin Lock with Low Coherence Traffic
lockit: LL R2, 0(R1) ; load linked, generates no coherence traffic
BNEZ R2, lockit ; not available, keep spinning
DADDUI R2, R0, #1 ; put value 1 in R2
SC R2, 0(R1) ; store-conditional succeeds if no one
; updated the lock since the last LL
BEQZ R2, lockit ; confirm that SC succeeded, else keep trying
If there are i processes waiting for the lock, how many
bus transactions happen?
1 write by the releaser + i (or 1) read-miss requests +
i (or 1) responses + 1 write by acquirer + 0 (i-1 failed SCs) +
i-1 (or 1) read-miss requests + i-1 (or 1) responses
(The i/i-1 read misses and responses can be reduced to 1)

## Slide 6
Lock Vs. Optimistic Concurrency
lockit: LL R2, 0(R1)
BNEZ R2, lockit
DADDUI R2, R0, #1
SC R2, 0(R1)
BEQZ R2, lockit
Critical Section
ST 0(R1), #0
tryagain: LL R2, 0(R1)
DADDUI R2, R2, R3
SC R2, 0(R1)
BEQZ R2, tryagain
LL-SC is being used to figure out
if we were able to acquire the lock
without anyone interfering – we
then enter the critical section
If the critical section only involves
one memory location, the critical
section can be captured within the
LL-SC – instead of spinning on the
lock acquire, you may now be spinning
trying to atomically execute the CS

## Slide 7
Coherence Vs. Consistency
Recall that coherence guarantees (i) that a write will
eventually be seen by other processors, and (ii) write
serialization (all processors see writes to the same location
in the same order)
The consistency model defines the ordering of writes and
reads to different memory locations – the hardware
guarantees a certain consistency model and the
programmer attempts to write correct programs with
those assumptions

## Slide 8
Example Programs
Initially, A = B = 0
P1 P2
A = 1 B = 1
if (B == 0) if (A == 0)
critical section critical section
Initially, A = B = 0
P1 P2 P3
A = 1
if (A == 1)
B = 1
if (B == 1)
register = A
Initially, Head = Data = 0
P1 P2
Data = 2000 while (Head == 0)
Head = 1 { }
… = Data

## Slide 9
Sequential Consistency
P1 P2
Instr-a Instr-A
Instr-b Instr-B
Instr-c Instr-C
Instr-d Instr-D
… …
We assume:
Within a program, program order is preserved
Each instruction executes atomically
Instructions from different threads can be interleaved arbitrarily
Valid executions:
abAcBCDdeE… or ABCDEFabGc… or abcAdBe… or
aAbBcCdDeE… or …..

## Slide 10
Problem 1
What are possible outputs for the program below?
Assume x=y=0 at the start of the program
Thread 1 Thread 2
x = 10 y=20
y = x+y x = y+x
Print y

## Slide 11
Problem 1
What are possible outputs for the program below?
Assume x=y=0 at the start of the program
Thread 1 Thread 2
A x = 10 a y=20
B y = x+y b x = y+x
C Print y
Possible scenarios: 5 choose 2 = 10
ABCab ABaCb ABabC AaBCb AaBbC
10 20 20 30 30
AabBC aABCb aABbC aAbBC abABC
50 30 30 50 30

## Slide 12
Sequential Consistency
Programmers assume SC; makes it much easier to
reason about program behavior
Hardware innovations can disrupt the SC model
For example, if we assume write buffers, or out-of-order
execution, or if we drop ACKS in the coherence protocol,
the previous programs yield unexpected outputs

## Slide 13
Consistency Example - I
An ooo core will see no dependence between instructions
dealing with A and instructions dealing with B; those
operations can therefore be re-ordered; this is fine for a
single thread, but not for multiple threads
Initially A = B = 0
P1 P2
A  1 B  1
… …
if (B == 0) if (A == 0)
Crit.Section Crit.Section
The consistency model lets the programmer know what assumptions
they can make about the hardware’s reordering capabilities

## Slide 14
Consistency Example - 2
Initially, A = B = 0
P1 P2 P3
A = 1
if (A == 1)
B = 1
if (B == 1)
register = A
If a coherence invalidation didn’t require ACKs, we can’t
confirm that everyone has seen the value of A.

## Slide 15
Sequential Consistency
A multiprocessor is sequentially consistent if the result
of the execution is achievable by maintaining program
order within a processor and interleaving accesses by
different processors in an arbitrary fashion
Can implement sequential consistency by requiring the
following: program order, write serialization, everyone has
seen an update before a value is read – very intuitive for
the programmer, but extremely slow
This is very slow… alternatives:
  Add optimizations to the hardware (e.g., verify loads)
  Offer a relaxed memory consistency model and fences

## Slide 16
Relaxed Consistency Models
We want an intuitive programming model (such as
sequential consistency) and we want high performance
We care about data races and re-ordering constraints for
some parts of the program and not for others – hence,
we will relax some of the constraints for sequential
consistency for most of the program, but enforce them
for specific portions of the code
Fence instructions are special instructions that require
all previous memory accesses to complete before
proceeding (sequential consistency)

## Slide 17
Fences
P1 P2
{ {
Region of code Region of code
with no races with no races
} }
Fence Fence
Acquire_lock Acquire_lock
Fence Fence
{ {
Racy code Racy code
} }
Fence Fence
Release_lock Release_lock
Fence Fence