## Slide 1
Lecture: Interconnection Networks
Topics: consistency model wrap-up, topologies, deadlock,
pipelines, switches, metrics

## Slide 2
Consistency Model Recap
Sequential Consistency Model
Programmer view Hardware view
Relaxed Consistency Model
Programmer view Hardware view
1. Each thread is sequential
2. Each instruction is atomic
3. Threads are arbitrarily interleaved
1. Disable ooo and speculation
2. Coherence protocol needs ACKs
1. Do not allow races
2. Encapsulate racy code with locks
3. Disciplined programs that are
easier to reason about
1. Support new fence instructions
2. Do not speculate past fences
3. Mostly OOO performance except
around fences

## Slide 3
Network Topology Examples
Grid
Hypercube
Torus

## Slide 4
Routing
Deterministic routing: given the source and destination,
there exists a unique route
Adaptive routing: a switch may alter the route in order to
deal with unexpected events (faults, congestion) – more
complexity in the router vs. potentially better performance
Example of deterministic routing: dimension order routing:
send packet along first dimension until destination co-ord
(in that dimension) is reached, then next dimension, etc.

## Slide 5
Deadlock
Deadlock happens when there is a cycle of resource
dependencies – a process holds on to a resource (A) and
attempts to acquire another resource (B) – A is not
relinquished until B is acquired

## Slide 6
Deadlock Example
Packets of message 1
Packets of message 2
Packets of message 3
Packets of message 4
4-way switch
Output ports
Each message is attempting to make a left turn – it must acquire an
output port, while still holding on to a series of input and output ports
Input ports

## Slide 7
Deadlock-Free Proofs
Number edges and show that all routes will traverse edges in
increasing (or decreasing) order – therefore, it will be impossible to
have cyclic dependencies
Example: k-ary 2-d array with dimension routing: first route along
x-dimension, then along y
1
2
3
2
1
0
1
2
3
2
1
0
1
2
3
2
1
0
1
2
3
2
1
0
17
18
19
18
17
16

## Slide 8
Breaking Deadlock
Consider the eight possible turns in a 2-d array (note that
turns lead to cycles)
By preventing just two turns, cycles can be eliminated
Dimension-order routing disallows four turns
Helps avoid deadlock even in adaptive routing
West-First
North-Last
Negative-First
Can allow
deadlocks

## Slide 9
Packets/Flits
A message is broken into multiple packets (each packet
has header information that allows the receiver to
re-construct the original message)
A packet may itself be broken into flits – flits do not
contain additional headers
Two packets can follow different paths to the destination
Flits are always ordered and follow the same path
Such an architecture allows the use of a large packet
size (low header overhead) and yet allows fine-grained
resource allocation on a per-flit basis

## Slide 10
Flow Control
The routing of a message requires allocation of various
resources: the channel (or link), buffers, control state
Bufferless: flits are dropped if there is contention for a
link, NACKs are sent back, and the original sender has
to re-transmit the packet
Circuit switching: a request is first sent to reserve the
channels, the request may be held at an intermediate
router until the channel is available (hence, not truly
bufferless), ACKs are sent back, and subsequent
packets/flits are routed with little effort (good for bulk
transfers)

## Slide 11
Virtual Channels
Buffers
Buffers
Flits do not carry headers. Once a packet starts going over a
channel, another packet cannot cut in (else, the receiving
buffer will confuse the flits of the two packets). If the packet is
stalled, other packets can’t use the channel.
With virtual channels, the flit can be received into one of N buffers.
This allows N packets to be in transit over a given physical channel.
The packet must carry an ID to indicate its virtual channel.
channel
Buffers
Buffers
Physical channel
Buffers
Buffers

## Slide 12
Virtual Channel Flow Control
Incoming flits are placed in buffers
For this flit to jump to the next router, it must acquire
three resources:
  A free virtual channel on its intended hop
    We know that a virtual channel is free when the
    tail flit goes through
  Free buffer entries for that virtual channel
    This is determined with credit or on/off management
  A free cycle on the physical channel
    Competition among the packets that share a
    physical channel

## Slide 13
Deadlock Avoidance with VCs
VCs provide another way to number the links such that
a route always uses ascending link numbers
2
1
0
1
2
3
2
1
0
1
2
3
2
1
0
1
2
3
2
1
0
17
18
19
18
17
16
102
101
100
101
102
103
117
118
119
118
117
116
202
201
200
201
202
203
217
218
219
218
217
216
Alternatively, use West-first routing on the
1st plane and cross over to the 2nd plane in
case you need to go West again (the 2nd
plane uses North-last, for example)

## Slide 14
Router Functions
Crossbar, buffer, arbiter, VC state and allocation,
buffer management, ALUs, control logic, routing
Typical on-chip network power breakdown:
  30% link
  30% buffers
  30% crossbar

## Slide 15
Router Pipeline
Four typical stages:
  RC routing computation: the head flit indicates the VC that it
  belongs to, the VC state is updated, the headers are examined
  and the next output channel is computed (note: this is done for
  all the head flits arriving on various input channels)
  VA virtual-channel allocation: the head flits compete for the
  available virtual channels on their computed output channels
  SA switch allocation: a flit competes for access to its output
  physical channel
  ST switch traversal: the flit is transmitted on the output channel
A head flit goes through all four stages, the other flits do nothing in the
first two stages (this is an in-order pipeline and flits can not jump
ahead), a tail flit also de-allocates the VC

## Slide 16
Router Pipeline
Four typical stages:
  RC routing computation: compute the output channel
  VA virtual-channel allocation: allocate VC for the head flit
  SA switch allocation: compete for output physical channel
  ST switch traversal: transfer data on output physical channel
RC
VA
SA
ST
--
--
SA
ST
--
--
SA
ST
--
--
SA
ST
Cycle 1 2 3 4 5 6 7
Head flit
Body flit 1
Body flit 2
Tail flit
RC
VA
SA
ST
--
--
SA
ST
--
--
SA
ST
--
--
SA
ST
SA
--
--
--
STALL

## Slide 17
Trends
Growing interest in eliminating the area/power overheads
of router buffers; traffic levels are also relatively low, so
virtual-channel buffered routed networks may be overkill
Option 1: use a bus for short distances (16 cores) and use
a hierarchy of buses to travel long distances
Option 2: hot-potato or bufferless routing

## Slide 18
Centralized Crossbar Switch
P1
P2
P3
P4
P5
P6
P7
P0

## Slide 19
Crossbar Properties
Assuming each node has one input and one output, a
crossbar can provide maximum bandwidth: N messages
can be sent as long as there are N unique sources and
N unique destinations
Maximum overhead: WN2 internal switches, where W is
data width and N is number of nodes
To reduce overhead, use smaller switches as building
blocks – trade off overhead for lower effective bandwidth

## Slide 20
Switch with Omega Network
P1
P2
P3
P4
P5
P6
P7
P0
000
001
010
011
100
101
110
111
111
110
101
100
011
010
001
000

## Slide 21
Omega Network Properties
The switch complexity is now O(N log N)
Contention increases: P0  P5 and P1  P7 cannot
happen concurrently (this was possible in a crossbar)
To deal with contention, can increase the number of
levels (redundant paths) – by mirroring the network, we
can route from P0 to P5 via N intermediate nodes, while
increasing complexity by a factor of 2

## Slide 22
Tree Network
Complexity is O(N)
Can yield low latencies when communicating with neighbors
Can build a fat tree by having multiple incoming and outgoing links
P0
P3
P2
P1
P4
P7
P6
P5

## Slide 23
Bisection Bandwidth
Split N nodes into two groups of N/2 nodes such that the
bandwidth between these two groups is minimum: that is
the bisection bandwidth
Why is it relevant: if traffic is completely random, the
probability of a message going across the two halves is
½ – if all nodes send a message, the bisection
bandwidth will have to be N/2
The concept of bisection bandwidth confirms that the
tree network is not suited for random traffic patterns, but
for localized traffic patterns

## Slide 24
Topology Examples
Grid
Hypercube
Torus
Criteria 64 nodes | Bus | Ring | 2Dtorus | Hypercube | Fully connected
Performance Bisection bandwidth |  |  |  |  | 
Cost Ports/switch Total links |  |  |  |  | 

## Slide 25
Topology Examples
Grid
Hypercube
Torus
Criteria 64 nodes | Bus | Ring | 2Dtorus | Hypercube | Fully connected
Performance Diameter Bisection BW | 1 1 | 32 2 | 8 16 | 6 32 | 1 1024
Cost Ports/switch Total links | 1 | 3 64 | 5 128 | 7 192 | 64 2016

## Slide 26
k-ary d-cube
Consider a k-ary d-cube: a d-dimension array with k
elements in each dimension, there are links between
elements that differ in one dimension by 1 (mod k)
Number of nodes N = kd
Number of switches :
Switch degree :
Number of links :
Pins per node :
Avg. routing distance:
Diameter :
Bisection bandwidth :
Switch complexity :
Should we minimize or maximize dimension?

## Slide 27
k-ary d-Cube
Consider a k-ary d-cube: a d-dimension array with k
elements in each dimension, there are links between
elements that differ in one dimension by 1 (mod k)
Number of nodes N = kd
Number of switches :
Switch degree :
Number of links :
Pins per node :
Avg. routing distance:
Diameter :
Bisection bandwidth :
Switch complexity :
N
2d + 1
Nd
2wd
d(k-1)/4
d(k-1)/2
2wkd-1
The switch degree, num links, pins per node, bisection bw for
a hypercube are half of what is listed above (diam and avg routing
distance are twice, switch complexity is ) because unlike
the other cases, a hypercube does not have right and left neighbors.
Should we minimize or maximize dimension?
(2d + 1)2
(d + 1)2